## Slide 1: Fundamental Principles of Airmanship
Learning Outcome 3 (Part): Know the Features and Types of Aircraft Used for Air Cadet Flying
Version 2 (May 19)

## Slide 2: Practical Activities
Undertake the practical activities found in Ultilearn and record their completion in the First Class Cadet Logbook.
and
Demonstrate and practice on a flight simulator, if you have one.

## Slide 3: Types of aircraft

## Slide 4: Viking T1
PASS
The Grob G103A Twin II Acro, known by the RAF as the Viking T1
Used by the RAF Air Cadets to give basic gliding training
Used by the Volunteer Gliding Squadrons
Two seat tandem with dual controls
Normally winch-launched but can be aero-towed

## Slide 5: Grob Tutor
PASS
Grob 115 (Tutor) T1
Primary trainer used for AEF and for elementary flying training by the UAS and RAF
Single engine, fixed wing monoplane
Two seat side-by-side with dual controls

## Slide 6
Wingspan: 10.0m
Length: 7.6m
Height: 2.8m
Max Weight: 990Kg
Engine: 180hp
Max Speed: 185 knots
Side-by-side 2 seat tandem
Carbon Fibre construction
Grob Tutor 115
PASS

## Slide 7: Cockpit Layout
PASS
Notes: General Cockpit Layout
The cockpit of the Tutor is simple compared with that of modern operational aircraft. Nevertheless there will be much in it that will be strange to you at first. Terms you need to know are “instruments”, which indicate what the aircraft is doing and “controls,” which are used to manoeuvre the aircraft.
Two radios provide both air-to-ground and air-to-air communication. One operates within the UHF band and one within the VHF band. It is important that cadet passengers do not interfere with any of the settings on the radio control boxes Engine Instruments and Controls. There are several instruments associated with the engine, the two most important are grouped on the left side of the flying instruments. There are also 3 controls for adjusting the engine performance mounted on the centre console.
Engine Instruments
RPM. The rpm gauge shows the speed at which the engine is rotating in revolutions per minute (rpm). The reading “20” gives 2,000 rpm.
Manifold Pressure (MP). This instrument gives an indication of how much power is being supplied by the engine, it responds to throttle movements and is calibrated in inches of mercury (it is the pressure in the engine inlet manifold).
Temperatures and Pressures. Two small instruments under the left (secondary) Attitude Indicator show various temperatures (in degrees Celsius) and pressures (in pounds per square inch – psi) within the engine.
Engine Controls
Throttle. The throttle lever is on the centre console. If pushed forward (opened), it increases the engine output – rather like the accelerator pedal on a car.
RPM Control. The RPM control is a blue lever to the right of the throttle, it enables the pilot to adjust the RPM of the engine and hence the efficiency of the propeller.
Mixture Control. The mixture control lever is the red lever next to the RPM control. It enables the pilot to adjust the fuel/air ratio of the mixture going into the engine

## Slide 8: Aircraft instruments
How to tell what an aeroplane is doing when in the air…

## Slide 9: Airspeed Indicator
MERIT
Shows the pilot the speed of the aircraft through the air,
  measured in knots
Assists the pilot in ensuring a stall does not occur
Helps the pilot keep a safe and constant speed
  Essential when navigating!

## Slide 10: Artificial Horizon Indicator
MERIT
Used to inform the pilot of the orientation of the aircraft relative to Earth's horizon
It indicates:
  pitch (fore and aft tilt)
  bank or roll (side to side tilt)

## Slide 11: Vertical Speed Indicator
Also called a Variometer
Used to inform the pilot of the rate of descent or climb of the aircraft
Is useful to help maintain level flight, especially during turning manoeuvres
MERIT

## Slide 12: Altimeter
MERIT
An instrument used to measure the altitude or height of an aircraft
Measured in feet
The pressure against which the altitude is being read is in the right hand window – this is changed by using the knob on the left
This altimeter is reading 920 feet above sea level
The big hand of the altimeter is the height in thousands, the one in the middle is the altitude in hundreds, the smallest one goes from 1 to 100

## Slide 13: Controls and planes of movement
How an aeroplane is controlled…

## Slide 14: Control Surfaces on an Aircraft
PASS
Elevator
Aileron
Aileron
Rudder

## Slide 15: Control Surfaces – what do they look like in real life?
Elevator
Aileron
Rudder
PASS

## Slide 16
Elevator
Aileron
Rudder
Control Surfaces – what do they look like in real life?
PASS

## Slide 17: The Axes of an Aircraft
DISTINCTION

## Slide 18: Longitudinal Axis – “roll”
Controlled by Ailerons
DISTINCTION

## Slide 19: Vertical Axis – “yaw”
Controlled by
the Rudder
DISTINCTION

## Slide 20: Lateral Axis – “pitch”
Controlled by Elevators
DISTINCTION

## Slide 21
DISTINCTION
Ailerons

## Slide 22
Control
column
Push right
DISTINCTION

## Slide 23
Left aileron down
Right aileron up
DISTINCTION

## Slide 24
Aircraft rolls right
DISTINCTION

## Slide 25
Aircraft rolls right
DISTINCTION

## Slide 26
And continues to do so until the
control column is placed
in the neutral position
Aircraft rolls right
DISTINCTION

## Slide 27: Summary
Control column left
Left aileron up
Right aileron down
Aircraft rolls left
DISTINCTION

## Slide 28
Rudder
DISTINCTION

## Slide 29
The rudder is controlled by
‘Rudder Pedals’ in the cockpit
DISTINCTION

## Slide 30
Rudder pedals
set to neutral
DISTINCTION

## Slide 31
Push right pedal forwards
(left will come back towards you!)
Rudder moves
right
DISTINCTION

## Slide 32
Aircraft yaws
right
DISTINCTION

## Slide 33
Aircraft yaws
right
DISTINCTION

## Slide 34
Aircraft yaws
right
DISTINCTION

## Slide 35: Summary
Push right pedal forward
Rudder moves right
Aircraft moves right
Push left pedal forward
Rudder moves left
Aircraft moves left
DISTINCTION

## Slide 36
Elevator
DISTINCTION

## Slide 37
Control
column
Push
Forward
DISTINCTION

## Slide 38
Elevator
moves
down
DISTINCTION

## Slide 39
Nose
pitches down
DISTINCTION

## Slide 40
Nose
pitches down
DISTINCTION

## Slide 41
Nose
pitches down
And continues to do so until the
control column is placed
in a neutral position
Airspeed will
increase
DISTINCTION

## Slide 42: Summary
Control column back
Elevator moves up
Nose pitches up
Speed will decrease
DISTINCTION

## Slide 43: Practical Activities
Undertake the practical activities found in Ultilearn and record their completion in the First Class Cadet Logbook.
and
Demonstrate and practice on a flight simulator, if you have one.